## Slide 1: Square Pad PCB Design
Elizabeth Starling, Jerry Collins
Florida Institute of Technology
High Energy Physics Lab A
January 26th, 2015

## Slide 2: Features
121 square pads
    9 mm x 9 mm each
    10 cm x 10 cm total active area
Four layers
  Top signal layer
  Middle ground layer
  Middle signal layer
    Bottom ground plane
Pad design (as opposed to strips) allows for precise determination of position with minimal pads/strips.
  Voltage can be applied directly to the HV pads, or via a high voltage divider
Vias allow routing underneath the pads on the mid-layer
All signal traces connect to a single Panasonic connector
Grounding between all signal traces to minimize crosstalk
    Two different grounding designs

## Slide 3: Design A (ground traces)
Top three rows are routed across to study the effect of pad-to-trace crosstalk.
Middle ground plane in-between top and middle signal layers to minimize crosstalk
Ground traces in-between each signal trace to minimize trace-to-trace crosstalk
Orange lines routed on mid-layer to yellow top layer
All signals connect to one Panasonic
HV
Divider
Area
Through-vias connect mid and top signal layers, and all ground layers
Ground traces between each signal trace

## Slide 4: Design B (ground Plane)
Solid ground plane (minimum clearance around signal traces)
Different approach
Utilizes solid ground planes instead of traces
Connects top, mid, and back ground planes